## Slide 1: Deriving Functional Properties of Components from the Analysis of Digital Mock-Ups
Ahmad Shahwan Jean-Claude Léon Gilles Foucault Lionel Fine
G-SCOP Laboratory Université de Grenoble, Grenoble-INP INRIA Rhone-Alpes
EADS
May 2012

## Slide 2: Outlines
Motivation
Related Works
Overview of our Approach
Conventional Interfaces
Detecting Geometric Interactions
Qualitative Reasoning Process
Application of Construction Rules
Conclusions and Future Works

## Slide 3: Motivation
Simplification
#CapScrew
#Nut
Semantic Annotation
Importance of Simplification for Finite Element Analysis.
Manual Simplification needs manpower.
Automated Simplification needs Semantic Information linked to a structured geometric model of components.
Our work comes to fill this gap.
Design Model
Simulation Model

## Slide 4: Related Works
Use of textual information to deduce semantics [Hang et al. 2006, Iyer et al. 2005, Min et al. 2008]
  No standards or norms  unreliable results.
Analyzing form features [Joshi et al. 1988, Zhu et al. 2002, Thakur et al. 2009]
  Adresses standalone components;
  Limited geometric complexity;
  Require user intervention.
Using assembly constraints to deduce geometric interactions [Schenk et al. 2005]
  Constraints are not always explicitly available (e.g. STEP files);
  One configuration can be expressed in different ways;
  Constraints are omitted for large DMUs.
Relation between shape, function and behavior is well-established [Albers et al. 2009, Gero 1990]

## Slide 5: Overview of our Approach
Input: A DMU represented as a STEP file.
Output: Semantic information, including mechanical and kinematic properties.
Contextual analysis of components: Conventional Interfaces (CIs) in an assembly model.
Functional interpretation of an interface: Functional Interface (FI)
Qualitative reasoning process to analyze components’ behaviors.
Taxonomy of Functional Designation (FD): deriving functional features of components from their FIs.
Structural geometric model of components that links to functional annotations.

## Slide 6: Conventional Interfaces
Real Shape: Shape of the physical body of a component.
Digital Shape: Possible volume, surface, or line model representing a component in a DMU.
Idealization
Real Shape
Digital Shape
Digital shapes are conventional representations of a component.
Digital shapes influence the interfaces between components in a DMU, leading to Conventional Interfaces (CIs).
Three categories of CIs
  Contact
  Interference
  Clearance
Simple Cylinder
Detailed Threaded Link

## Slide 7: Detecting Geometric Interactions
CI are structured to build the Conventional Interface Graph (CIG).
CIG(C, CI): C set of components in a DMU, CI set of conventional interfaces.

## Slide 8: Detecting Geometric Interactions
Detection of CIs
  Geometric processing of the DMU.
  Geometric modelers lack performance and are not robust enough.
  The need for specific algorithms.
Detection of Linear Contacts
CAD Model
Results using OCCT
Our Results
?

## Slide 9: Qualitative Reasoning Process
Due to idealization, one CI can be associated to more than one Functional Interface (FI), considering only its geometry.
Reduce the number of FIs to ideally one per CI.
To this end, use a qualitative reasoning process based on the concept of Reference State.
Cylindrical Interference
Threaded Coupling
Spline Coupling
?
Conventional Interface
Functional Interface

## Slide 10: Qualitative Reasoning Process
General hypothesis
  Interfaces between components are time-invariant.
  Components are rigid bodies
Reference State: Description of physical and qualitative behavior of a DMU. In our analysis reference states materialize as hypothesis.
Mechanical Reference State
  Hypothesis: Assembly is at rest; thus, all components of a DMU are in static equilibrium.
  Reasoning upon this reference state is based on the real shape/force duality.
Kinematic Reference State
  Hypothesis: Unless justified by a functional kinematic chain, all internal motion in a DMU are rotational.
  Reasoning upon this reference state is based on the real shape/kinematics duality.

## Slide 11: Mechanical Analysis
Planar Contact
Cylindrical Interference
Spline Link
Planar Support
Threaded Link
Planar Support
Unbalanced
Balanced
interpretations
All components are at static equilibrium;
For each component
  External forces sum up to zero, and
  Moment of external forces sum up to zero around all axes.
FI that violate this hypothesis are eliminated.

## Slide 12: Mechanical Analysis
Initial (null) screw
Planar Support
Threaded Coupling
Spline Coupling
Nullable Screw
Non-nullable Screw


Three structure: levels are CIs, nodes are FIs.
All Solutions algorithm V.S. Best Solution algorithm.
1
1
2
Use of mechanical screws to represent forces and moments.
Qualitative reasoning  Qualitative values.
Value | Null | Not null | Strictly Positive | Strictly Negative | Arbitrary
Symbol | 0 | ± | + | - | *
Constraint | x = 0 | x ≠ 0 | x > 0 | x < 0 | Non

## Slide 13
Examples
Initialization
All-solutions method
Best-solution method
#0
#38
#3
#28
#2

## Slide 14: Application of Construction Rules
Domain specific rules enable:
  The elimination of inconsistent solutions,
  The assignment of component FD.
To enable dynamic domain rules, rules and taxonomies are represented using an ontology.
The ontology is then instantiated with information coming from reference state analysis, producing the DMU’s knowledge base.
Reasoning upon this KB, applying domain (construction) rules, leads to the classification of components into FD classes.

## Slide 15: Using a Knowledge Base
Knowledge Base (Ontology)
…
Screw
Nut
Component
…
Threaded Link
Planar Support
Conventional Interface
x
y
a
b
x
y
a
a
inner-forms
outer-forms
x
y
b
b
forms
forms
Nut
----
Screw 
----
Initialization
  Concepts
  Rules
Instantiation
  Individuals
  Relations
Reasoning
  Classification
Domain Expertise
Ref. Sate Analysis

## Slide 16: Example of FD
Screw
Nut
Counter-nut

## Slide 17: Conclusions and Future Work
Our results confirm the utility of exploiting interactions between components in a DMU to deduce functional information.
Qualitative reasoning based on pure geometry:
  Algorithmic analysis of geometric configuration under a given reference state.
  Rule-based reasoning inspired by domain knowledge.
Further work:
  Identification of other reference states to enrich the knowledge base with new facts about the DMU.
  Recognition of components functional designations
Acknowledgment: work conducted in the scope of the ROMMA project funded by ANR.

## Slide 18: References
Hong T., Lee K., Kim S., Similarity comparison of mechanical parts to reuse existing designs. CAD 38 (2006), 973–984.
Iyer N., Jayanti S., Lou K., Kalyanaraman Y., Ramani K., Shape-based searching for product lifecycle applications. CAD 37 (2005), 1435–1446.
Min P., Halderman J., Kazhdan M., Funkhouser T., Early experiences with a 3d model search engine. 8th Int. Conf. 3D Web Tech. (2003), 7–19.
Joshi S., Chang T. C., Graph-based heuristics for recognition of machined features from a 3D solid model. Comput. Aided Des. (1988), 20(2), 58—66.
Zhu H., Menq C. H., B-Rep model simplification by automatic fillet/round suppressing for efficient automatic feature recognition, Comput. Aided Des. (2002), 34(2), 109—123.
Thakur A., Banerjee A. G., Gupta S. K., A survey of CAD model simplification techniques for physics-based simulation applications, Comput. Aided Des. (2009), 41(2), 65—80.
Schenk M., Straßburger S., Kissner H., Combining Virtual Reality and Assembly Simulation for Production Planning and Worker Qualification. Int. Conf. Changeable, Agile, Reconfigurable and Virtual Production (2005),11—414.
Albers A., Braun A., Clarkson P. J., Enkler H.-G., Wynn D., Contact and channel modelling to support early design of technical systems, ICED (2009), 61—72.
Gero J. S., Design prototypes: a knowledge representation schema for design. AI Magazine (1990), 11 (4) 26–36.